## Slide 1: Workshop on Robotic Simulation
Robo Carnival 2023

## Slide 2: Introduction to the software
Interface
Scene, navigation (Pan, rotate, zoom)
Placing basic objects (Move, rotate, scale)
Object properties (Static, Dynamic, Respondable, Non-respondable)
Model Browser – pick and place (Mobile robot, Stationary robot)
Scene Hierarchy
Scripts

## Slide 3: Types of Robots
Mobile Robot
Non-mobile Robot

## Slide 4: Robot Structure
Link
Joint
Scene Hierarchy

## Slide 5: Robot Structure
Link
Joint
Scene Hierarchy

## Slide 6: Robot Joints
Revolute Joint (Rotational- 1 Axis)
Prismatic Joint (Translational – 1 Axis)
Spherical Joint
(Rotational- 3 Axis)

## Slide 7: Actuators
Position Control
Velocity Control

## Slide 8: Sensors
Proximity/Distance Sensor
Equivalent to Ultrasound/IR proximity
Vision Sensor
Orthographic
Perspective

## Slide 9: Line Following Robot Build
Body of the Robot (1 Cuboid)
  Add > Primitive shape > Cuboid
  Dimension (10cm x 10cm x 0.5cm)
  Default unit is in meters
Wheels of the Robot (4 Cylinder)
  Add > Primitive shape > Cylinder
  Dimension (5cm x 2cm)
Motors of the Robot (4 Joints)
  Add > Joint > Revolute

## Slide 10: Colors
Double click cuboid icon
Object Properties > Color
Shape > Ambient/diffuse
Components
Adjust color parameters

## Slide 11: Joints
Double click joint icon
Object Properties > Visual Properties
Adjust the values
This changes appearance only,
no effect on joint behavior

## Slide 12: Renaming
Double click on name of object
Set appropriate name
Hit enter to set name

## Slide 13: Link-Joint-Link
Drag and drop objects to set the appropriate object hierarchy.
Body should be first link
Joints are child of body
Each wheel is child of a joint

## Slide 14: Moving Objects
Select a joint/object
Click on translation icon
With mouse translation tab active,
drag the object around
Child objects will move with parent

## Slide 15: Rotating Objects
Select a joint/object
Click on rotation icon
Go to Rotation tab
Select Own frame
Around X [deg] > 90
Click X-rotate sel

## Slide 16: Enable Motor
Double click joint icon
Dynamic properties dialog
Control mode > Velocity
Set velocity to 0

## Slide 17: Line Following Robot - Lua
https://www.coppeliarobotics.com/helpFiles/en/lineFollowingBubbleRobTutorial.htm

## Slide 18: Line Following Robot - Python
https://www.coppeliarobotics.com/helpFiles/en/remoteApiFunctionsPython.htm