## Slide 1: Workshop on Robotic Simulation
Robo Carnival 2023

## Slide 2: Vision Sensor Feedback
To see what is seen by each vision sensor, we need to add Floating view
On any empty space in the simulation window, Right click > Add > Floating view

## Slide 3: Vision Sensor Feedback
To see what is seen by each vision sensor, we need to add Floating view
On any empty space in the simulation window, Right click > Add > Floating view
Drag and resize the window as necessary
Select a vision sensor from Scene hierarchy
On the created floating view > Right Click > View > Associate view with selected vision sensor
Vision sensor output should be visible if the simulation is started

## Slide 4: Line Following Robot - Lua
Scripts are responsible for controlling inside the simulation
To create a script for any object (robot/joint/dummy shape) we simply select object > right click > Add > Associated child script > Non-threaded > Lua
We will convert a demo Lua script from the CoppeliaSim documentation to create a code for our own robot: https://www.coppeliarobotics.com/helpFiles/en/lineFollowingBubbleRobTutorial.htm

## Slide 5: Creating a Line for Following
To create a line following path, Add > Path > Closed
A circular path will be created

## Slide 6: Creating a Line for Following
To increase the path size, on the path dummy icon, double click > Scene Object Properties > Common > Scaling > Scaling factor = 5
This will scale the path size by a factor of 5
To move around the path control points, simply select them from the Scene Hierarchy and then use the translate tool to create paths of any arbitrary shape

## Slide 7: Creating a Line for Following
Path shaping

## Slide 8: Creating a Line for Following
Now we need to give visual properties to the path. On the script icon aside the path object, double click to open script
section indicates the render properties of the path. According to the documentation, replace the line with:
local section={-0.02,0.001,0.02,0.001}
color indicates path color in RGB format. We can change it to {0.2, 0.2, 0.2} for a dark gray color
After modifying script, click on the Restart Script icon on the top left of the script editor for changes to take effect

## Slide 9: Creating a Line for Following
Double click on the parameters icon > Check Generate extruded shape
The path will take our desired black color. Drag the robot to any place on the path

## Slide 10: Robot Code - Lua
To create a script for our robot, select object > right click > Add > Associated child script > Non-threaded > Lua
We will copy and paste the example LFR script from the last part of the documentation page and modify it for our robot: https://www.coppeliarobotics.com/helpFiles/en/lineFollowingBubbleRobTutorial.htm
The following slides are based on the provided part2_LFR_LUA.ttt file

## Slide 11: Code Structure
An empty non-threaded script has the following parts:
  function sysCall_init()
    Does all the initialization for the associated object
    Runs once after starting simulation
  function sysCall_sensing()
    Called during each loop to collect sensor data
  function sysCall_actuation()
    Called during each loop after sensor data is received
    Sends commands to the actuators for moving the robot
  function sysCall_cleanup()
    Called after end of simulation
Any custom function can be added for ease of coding
Initialization
Sensing
Actuation
Termination
General system flow for any robot

## Slide 12: Object Handles
During sysCall_init(), we need to find the references for motors and sensors.
In real hardware, we initialize the microcontroller pins in this stage.
In simulation, we fetch the object handles
For our simulation, we first find the 4 motors by their exact name in the scene hierarchy (duplicate names are not allowed in simulation)
    leftMotor1=sim.getObject("./Motor_FL")
    leftMotor2=sim.getObject("./Motor_BL")
    rightMotor1=sim.getObject("./Motor_FR")
    rightMotor2=sim.getObject("./Motor_BR")
leftMotor1
rightMotor1
leftMotor2
rightMotor2
Robot structure

## Slide 13: Object Handles
We find the 5 vision sensors, and save the handles to an array for easy access
    line_sensor_handle={-1,-1,-1,-1,-1}
    line_sensor_handle[1]=sim.getObject("./Vis[4]")
    line_sensor_handle[2]=sim.getObject("./Vis[3]")
    line_sensor_handle[3]=sim.getObject("./Vis[2]")
    line_sensor_handle[4]=sim.getObject("./Vis[1]")
    line_sensor_handle[5]=sim.getObject("./Vis[0]")
leftMotor1
rightMotor1
leftMotor2
rightMotor2
Robot structure

## Slide 14: Reading Sensor Data
After initialization, the code enters a loop of reading sensors and acting based on the readings
In a smaller loop, the code takes the reading of each sensor one by one by the following function: result,data=sim.readVisionSensor(line_sensor_handle[i])
‘result’ tells us whether the sensor was properly read
‘data’ contains the actual reading
‘data’ is a list of values, data[11] contains the average pixel value, so we use that information for detecting lines
data[11] is thresholded by comparing to 0.5 sensorReading[i]=(data[11]<0.5)
  If data[11] < 0.5; sensor is on black line
  If data[11] > 0.5; sensor is not on black line

## Slide 15: Adjusting Motor Velocities
leftMotor1
rightMotor1
leftMotor2
rightMotor2
Line is on left of robot
Right motors speed increase
Left motors speed decrease
leftMotor1
rightMotor1
leftMotor2
rightMotor2
Line is on right of robot
Right motors speed decrease
Left motors speed increase

## Slide 16: Adjusting Motor Velocities
The sensor readings give us an idea of where the line is relative to the robot
  If the right-most sensor is on line, then the robot is on the left, and we need to go right
    Increase speed of left motors
    if sensorReading[1] then
    leftV=0.03*speed
    end
  If the left-most sensor is on line, then the robot is on the right, and we need to go left
    Increase speed of right motors
    if sensorReading[5] then
    rightV=0.03*speed
    end
Finally send target velocity information to the motors:
  sim.setJointTargetVelocity(leftMotor1,leftV)
  sim.setJointTargetVelocity(leftMotor2,leftV)
  sim.setJointTargetVelocity(rightMotor1,rightV)
  sim.setJointTargetVelocity(rightMotor2,rightV)

## Slide 17: Running the Simulation