## Slide 1: Workshop on Robotic Simulation
Robo Carnival 2023

## Slide 2: Remote APIs
CoppeliaSim has support for web-socket based remote APIs for Python, MATLAB, C/C++, Java, Octave
We can use remote APIs to run external code scripts to control robots via these languages
This is useful because Python has rich libraries for planning, computer vision and machine learning / deep learning
Remote APIs can work in the two modes:
  Asynchronous mode: Simulation and scripts run independently. Recommended for realistic simulations.
  Synchronous mode: Remote script will send commands to the simulator for stepping the simulation. Recommended for slower systems where data transfer between simulator and API is slow.

## Slide 3: Using Python Remote API
Python remote API documentation is a mandatory reference for us to find the necessary functions: https://www.coppeliarobotics.com/helpFiles/en/remoteApiFunctionsPython.htm
We need to copy some files to the source directory of the python script/notebook
    C:\Program Files\CoppeliaRobotics\CoppeliaSimEdu\programming\legacyRemoteApi\remoteApiBindings\lib\lib\Windows\remoteApi.dll
    C:\Program Files\CoppeliaRobotics\CoppeliaSimEdu\programming\legacyRemoteApi\remoteApiBindings\python\python\sim.py
    C:\Program Files\CoppeliaRobotics\CoppeliaSimEdu\programming\legacyRemoteApi\remoteApiBindings\python\python\simConst.py

## Slide 4: Python Remote API Example
  The following file contains an example code on how to use the Python API for controlling a simulation-
  C:\Program Files\CoppeliaRobotics\CoppeliaSimEdu\programming\legacyRemoteApi\remoteApiBindings\python\python\simpleTest.py
  The simulation has to be set up for socket connection. Add a child script to any of the objects inside the simulation and open a port for communication with a remote API:
    simRemoteApi.start(19999) // asynchronous mode
    19999 is the port number. The remote API will connect to this port. If running multiple simulations, each should have a separate port number.

## Slide 5: Code Structure
Python script needs the sim.py module to access the API
First we establish a socket connection with the simulator on the designated port
clientID=sim.simxStart('127.0.0.1',19999,True,True,5000,5)
The clientID will be required for further use
Next we need to fetch the handles for the robot joints and sensors
After initialization, we will receive sensor data and send actuator commands using the remote API to run the robot
Initialization
Sensing
Actuation
Termination
General system flow for any robot

## Slide 6: Object Handles
For getting general object handles:
returnCode, handle = sim.simxGetObjectHandle(clientID, objectPath, operationMode)
- returnCode : A return code on whether the operation was successful. Successful operations will return 0. Further details can be found here: https://www.coppeliarobotics.com/helpFiles/en/remoteApiConstants.htm#functionErrorCodes
- handle: Reference for accessing the object
- clientID: Reference to the remote connection to the simulation
- objectPath: Name of the object inside the simulation, should be a string
- operationMode: How the function will communicate with the simulator. Will be discussed in details later. The documentation on operation modes: https://www.coppeliarobotics.com/helpFiles/en/remoteApiConstants.htm#operationModes

## Slide 7: Actuator Objects
Getting the actuator handle:
err, leftMotor1 =sim.simxGetObjectHandle(clientID, '/Motor_FL', sim.simx_opmode_blocking)
- We set operating mode to simx_opmode_blocking. This means the function will halt the simulation until the function returns the desired information. We use blocking mode for functions that will be called only once during the simulation
Sending commands to actuator:
sim.simxSetJointTargetVelocity(clientID, leftMotor1, leftV, sim.simx_opmode_oneshot)
- simx_opmode_oneshot is used for sending commands to the simulator. The simulator does not send any acknowledgement of whether the command was received. Sending joint data in the blocking mode is not recommended since we will be continuously sending this.

## Slide 8: Vision Sensor Functions
returnCode, resolution, image = simxGetVisionSensorImage(clientID, sensorHandle, options, operationMode)
- This function will return the actual image sent by the sensor. Useful for full resolution images.
- resolution is an array containing the resolution of the returned image as set in the simulation
- image is an array object that will contain the image data
- options for receiving image, grayscale/RGB
- operationMode: for the first time this function is called, it should be set in streaming mode to let the simulator know that we will be receiving stream of information. For the consecutive calls, it should be buffer mode.
Alternate Function
returnCode, detectionState, auxPackets = simxReadVisionSensor(clientID, sensorHandle, operationMode)
- This function will return image statistics such as average value, min, max etc.
- auxPackets: by default CoppeliaSim returns one packet of 15 auxiliary values:the minimum of {intensity, red, green, blue, depth value}, the maximum of {intensity, red, green, blue, depth value}, and the average of {intensity, red, green, blue, depth value}

## Slide 9: Vision Sensor Objects
Getting the vision sensor handle (run once):
err, sensorHandle[0] = sim.simxGetObjectHandle(clientID, '/Vis_0', sim.simx_opmode_blocking)
- We use blocking mode for getting vision sensor handle
Establish communication stream (run once):
err, _ , _ = sim.simxReadVisionSensor(clientID, sensorHandle[0], sim.simx_opmode_streaming)
- We are letting the simulator know that we will be streaming this data
- Since the LFR is using one pixel only, knowing the average pixel intensity is good enough
- So we use the ReadVisionSensor() function
Reading buffered vision sensor data from simulation:
err, _ , value = sim.simxReadVisionSensor(clientID, sensorHandle[0], sim.simx_opmode_buffer) sensorReading[i] = value[0][11]<0.5
- 11th packed value is the average pixel intensity seen by the vision sensor
- Threshold it with respect to 0.5 to know whether sensor on line

## Slide 10: Head Over to the Code!
Line_follower.ipynb notebook contains the code for controlling the LFR in the part3_LFR_python.ttt
To open the notebook:
  Open the command line (cmd.exe - windows)/ terminal window (linux) in the notebook directory
  Activate the conda environment by typing “conda activate env_name”
  Start jupyter notebook by typing “jupyter notebook”
If you do not wish to use jupyter notebook, you can open the notebook in any other software (visual studio code/PyCharm) and copy the code to a .py file first.
Run the simulation first, and then run the python notebook / script to take control of the robot inside the simulation.